## Slide 1: 第 14 讲
单周期处理设计-数据通路

## Slide 2: 学习内容
选择MIPS指令集的一个子集作为CPU的实现目标
  下条指令地址计算与取指令部件
  R型指令的数据通路
  访存指令的数据通路
  立即数运算指令的数据通路
  分支和跳转指令的数据通路
综合所有指令的数据通路

## Slide 3: 学习目标
能够设计出各条指令的数据通路，至少要理解每条指令的数据通路是怎么来的

## Slide 4: 复习：MIPS的三种指令类型
ADD and SUBSTRACT
  add rd, rs, rt
  sub rd, rs, rt
OR Immediate:
  ori rt, rs, imm16
LOAD and STORE
  lw rt, rs, imm16
  sw rt, rs, imm16
BRANCH:
  beq rs, rt, imm16
JUMP:
  j target
op
target address
0
26
31
6 bits
26 bits
op
rs
rt
rd
shamt
func
0
6
11
16
21
26
31
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits
op
rs
rt
immediate
0
16
21
26
31
6 bits
16 bits
5 bits
5 bits
这些指令具有代表性！
有算术运算、逻辑运算；有RR型、RI型；有访存指令；有条件转移、无条件转移。
本讲目标：实现以上7条指令对应的数据通路！
教材中实现了11条指令，可将7条指令和11条指令的数据通路进行对比，以深入理解设计原理。
大家记得是哪三种类型？
R-Type、I-Type、J-Type
Notes: In today’s lecture, I will show you how to implement the following subset of MIPS instructions: add, subtract, or immediate, load, store, branch, and the jump instruction.
The Add and Subtract instructions use the R format. The Op together with the Func fields together specified all the different kinds of add and subtract instructions.
Rs and Rt specifies the source registers. And the Rd field specifies the destination register.
The Or immediate instruction uses the I format. It only uses one source register, Rs. The other operand comes from the immediate field. The Rt field is used to specified the destination register.
Both the load and store instructions use the I format and both add the Rs and the immediate filed together to form the memory address.
The difference is that the load instruction will load the data from memory into Rt while the store instruction will store the data in Rt into the memory.
The branch on equal instruction also uses the I format. Here Rs and Rt are used to specify the registers we need to compare.
If these two registers are equal, we will branch to a location specified by the immediate field.
Finally, the jump instruction uses the J format and always causes the program to jump to a memory location specified in the address field.
I know I went over this rather quickly and you may have missed something. But don’t worry, this is just an overview. You will keep seeing these (point to the format) all day today.
+3 = 13 min. (X:53)

## Slide 5: 设计处理器的步骤
第一步：分析每条指令的功能，并用RTL(Register Transfer Language) 来表示。
第二步：根据指令的功能给出所需的元件，并考虑如何将他们互连。
第三步：确定每个元件所需控制信号的取值。
第四步：汇总所有指令所涉及到的控制信号，生成指令与控制信号关系表。
第五步：根据表得到每个控制信号的逻辑表达式，据此设计控制器电路。
处理器设计涉及到数据通路的设计和控制器的设计
数据通路中有两种元件
  操作元件：由组合逻辑电路实现
  存储（状态）元件：由时序逻辑电路实现
ISA确定后，进行处理器设计的大致步骤
Notes: So let’s design a processor. How and where do we start?
Well, the best place to start is the processor’s instruction set architecture. After all, the goal of your design is to execute the instructions in the instruction set correctly.
What you need to do is to describe each instruction’s operation in register transfer language.
By looking at the Register Transfer Language description of the instruction, you can figure out the datapath components you need and how to connect these components together.
As I will show you, each datapath component will have its own set of control signals.
And the last step of the processor design task is to design the control unit that generates the control signals for the datapath.
So what do we mean by Register Transfer Language?
+2 = 27 min. (Y:07)

## Slide 6: 要设计实现的7条指令
实现目标（7条指令）：
ADD and subtract
  add rd, rs, rt
  sub rd, rs, rt
OR Immediate:
  ori rt, rs, imm16
LOAD and STORE
  lw rt, rs, imm16
  sw rt, rs, imm16
BRANCH:
  beq rs, rt, imm16
JUMP:
  j target
op
rs
rt
rd
shamt
func
0
6
11
16
21
26
31
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits
op
rs
rt
immediate
0
16
21
26
31
6 bits
16 bits
5 bits
5 bits
op
target address
0
26
31
6 bits
26 bits
Notes: In today’s lecture, I will show you how to implement the following subset of MIPS instructions: add, subtract, or immediate, load, store, branch, and the jump instruction.
The Add and Subtract instructions use the R format. The Op together with the Func fields together specified all the different kinds of add and subtract instructions.
Rs and Rt specifies the source registers. And the Rd field specifies the destination register.
The Or immediate instruction uses the I format. It only uses one source register, Rs. The other operand comes from the immediate field. The Rt field is used to specified the destination register.
Both the load and store instructions use the I format and both add the Rs and the immediate filed together to form the memory address.
The difference is that the load instruction will load the data from memory into Rt while the store instruction will store the data in Rt into the memory.
The branch on equal instruction also uses the I format. Here Rs and Rt are used to specify the registers we need to compare.
If these two registers are equal, we will branch to a location specified by the immediate field.
Finally, the jump instruction uses the J format and always causes the program to jump to a memory location specified in the address field.
I know I went over this rather quickly and you may have missed something. But don’t worry, this is just an overview. You will keep seeing these (point to the format) all day today.
+3 = 13 min. (X:53)

## Slide 7: 加法和减法指令(R-type类型）
实现目标（7条指令）：
ADD and subtract
  add rd, rs, rt
  sub rd, rs, rt
OR Immediate:
  ori rt, rs, imm16
LOAD and STORE
  lw rt, rs, imm16
  sw rt, rs, imm16
BRANCH:
  beq rs, rt, imm16
JUMP:
  j target
首先考虑add和sub指令（R-Type指令的代表）
op
rs
rt
rd
shamt
func
0
6
11
16
21
26
31
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits
op
rs
rt
immediate
0
16
21
26
31
6 bits
16 bits
5 bits
5 bits
op
target address
0
26
31
6 bits
26 bits
Notes: In today’s lecture, I will show you how to implement the following subset of MIPS instructions: add, subtract, or immediate, load, store, branch, and the jump instruction.
The Add and Subtract instructions use the R format. The Op together with the Func fields together specified all the different kinds of add and subtract instructions.
Rs and Rt specifies the source registers. And the Rd field specifies the destination register.
The Or immediate instruction uses the I format. It only uses one source register, Rs. The other operand comes from the immediate field. The Rt field is used to specified the destination register.
Both the load and store instructions use the I format and both add the Rs and the immediate filed together to form the memory address.
The difference is that the load instruction will load the data from memory into Rt while the store instruction will store the data in Rt into the memory.
The branch on equal instruction also uses the I format. Here Rs and Rt are used to specify the registers we need to compare.
If these two registers are equal, we will branch to a location specified by the immediate field.
Finally, the jump instruction uses the J format and always causes the program to jump to a memory location specified in the address field.
I know I went over this rather quickly and you may have missed something. But don’t worry, this is just an overview. You will keep seeing these (point to the format) all day today.
+3 = 13 min. (X:53)

## Slide 8: RTL: The ADD Instruction（加法指令）
op
rs
rt
rd
shamt
func
0
6
11
16
21
26
31
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits
add rd, rs, rt
  M[PC] 从PC所指的内存单元中取指令
  R[rd] ← R[rs] + R[rt] 从rs、rt 所指的寄存器中取数后相加。若结果不溢出，则将结果送rd 所指的寄存器中；若结果溢出，则不送结果，并转到“溢出处理程序”执行。
  PC ← PC + 4 PC加4，使PC指向下一条指令
Notes: Here is an example. In terms of Register Transfer Language, this is what the Add instruction need to do.
First, you need to fetch the instruction from memory.
Then you perform the actual add operation.
And finally, you need to update the program counter to point to the next instruction.
+1 = 28 min. (Y:08)

## Slide 9: RR（R-type）型指令的数据通路
功能：R[rd] ← R[rs] op R[rt]，如：add rd, rs, rt
32
Result
ALUctr
Clk
busW
RegWr
32
32
busA
32
busB
5
5
5
Rw
Ra
Rb
32 32-bit
Registers
rs
rt
rd
ALU
不考虑公共操作，仅R-Type指令执行阶段的数据通路如下：
ALUctr,RegWr: 指令译码后产生的控制信号
  Ra, Rb, Rw 分别对应指令的rs, rt, rd
“add rd, rs, rt”控制信号为？
ALUctr=add，RegWr=1
op
rs
rt
rd
shamt
func
0
6
11
16
21
26
31
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits
溢出时，不写结果并需转异常处理程序
溢出
寄存器组结构
Notes: And here is the datapath that can do the trick.
First of all, we connect the register file’s Ra, Rb, and Rw input to the Rd, Rs, and Rt fields of the instruction bus (points to the format diagram).
Then we need to connect busA and busB of the register file to the ALU.
Finally, we need to connect the output of the ALU to the input bus of the register file.
Conceptually, this is how it works.
The instruction bus coming out of the Instruction memory will set the Ra and Rb to the register specifiers Rs and Rt.
This causes the register file to put the value of register Rs onto busA and the value of register Rt onto busB, respectively.
But setting the ALUctr appropriately, the ALU will perform either the Add and Subtract for us.
The result is then fed back to the register file where the register specifier Rw should already be set to the instruction bus’s Rd field.
Since the control, which we will design in our next lecture, should have already set the RegWr signal to 1, the result will be written back to the register file at the next clock tick (points to the Clk input).
+3 = 42 min. (Y:22)

## Slide 10: 带立即数的逻辑指令（ori指令）
实现目标（7条指令）：
ADD and subtract
  add rd, rs, rt
  sub rd, rs, rt
OR Immediate:
  ori rt, rs, imm16
LOAD and STORE
  lw rt, rs, imm16
  sw rt, rs, imm16
BRANCH:
  beq rs, rt, imm16
JUMP:
  j target
2. 考虑ori 指令（I-Type指令和逻辑运算指令的代表）
op
rs
rt
rd
shamt
func
0
6
11
16
21
26
31
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits
op
rs
rt
immediate
0
16
21
26
31
6 bits
16 bits
5 bits
5 bits
op
target address
0
26
31
6 bits
26 bits
Notes: In today’s lecture, I will show you how to implement the following subset of MIPS instructions: add, subtract, or immediate, load, store, branch, and the jump instruction.
The Add and Subtract instructions use the R format. The Op together with the Func fields together specified all the different kinds of add and subtract instructions.
Rs and Rt specifies the source registers. And the Rd field specifies the destination register.
The Or immediate instruction uses the I format. It only uses one source register, Rs. The other operand comes from the immediate field. The Rt field is used to specified the destination register.
Both the load and store instructions use the I format and both add the Rs and the immediate filed together to form the memory address.
The difference is that the load instruction will load the data from memory into Rt while the store instruction will store the data in Rt into the memory.
The branch on equal instruction also uses the I format. Here Rs and Rt are used to specify the registers we need to compare.
If these two registers are equal, we will branch to a location specified by the immediate field.
Finally, the jump instruction uses the J format and always causes the program to jump to a memory location specified in the address field.
I know I went over this rather quickly and you may have missed something. But don’t worry, this is just an overview. You will keep seeing these (point to the format) all day today.
+3 = 13 min. (X:53)

## Slide 11: RTL: The OR Immediate Instruction
ori rt, rs, imm16
  M[PC] 取指令（公共操作，取指部件完成）
  R[rt] ← R[rs] or ZeroExt(imm16) 立即数零扩展，并与rs内容做“或”运算
  PC ← PC + 4 计算下地址（公共操作，取指部件完成）
imm16
0
16
15
31
16 bits
16 bits
0000 0000 0000 0000
零扩展 ZeroExt(imm16)
思考：应在前面数据通路上加哪些元件和连线？用何控制信号？
op
rs
rt
imm16
0
16
21
26
31
6 bits
16 bits
5 bits
5 bits
Notes: The or immediate is a I-type instruction.
The immediate field of the instruction (Imm16 of the format diagram) is zero extended to 32 bits before it is operated with the other operand.
The other operand is selected by the Rs field of the instruction.
The destination register of this instruction will be selected by the Rt field.
+2 = 57 min. (Y:27)

## Slide 12: 带立即数的逻辑指令的数据通路
R[rt] ← R[rs] op ZeroExt[imm16]] Example: ori rt, rs, imm16
32
Result
ALUctr
Clk
busW
RegWr
32
32
busA
32
busB
5
5
5
Rw
Ra
Rb
32 32-bit
Registers
Rs
Don’t Care
(Rt)
ALU
R-Type类型的结果写入Rd
R-Type的操作数来自busB
应加兰色部分，为什么？
Ori指令的控制信号：RegDst=？；RegWr=？；ALUctr=？；ALUSrc=？
Ori指令的控制信号：RegDst=1；RegWr=1；ALUSrc=1；ALUctr=or
Rt
Rd
RegDst
Mux
0
1
Ext
Mux
16
32
imm16
ALUSrc
0
1
op
rs
rt
imm16
0
16
21
26
31
6 bits
16 bits
5 bits
5 bits
Notes: Here is the datapath for the Or immediate instructions.
We cannot use the Rd field here (Rw) because in this instruction format, we don’t have a Rd field. The Rd field in the R-type is used here as part of the immediate field.
For this instruction type, Rw input of the register file, that is the address of the register to be written, comes from the Rt field of the instruction.
Recalled from earlier slide that for R-type instruction, the Rw comes from the Rd field.
That’s why we need a MUX here to put Rd onto Rw for R-type instructions and to put Rt onto Rw for the I-type instruction.
Since the second operation of this instruction will be the immediate field zero extended to 32 bits, we also need a MUX here to block off bus B from the register file.
Since bus B is blocked off by the MUX, the value on bus B is don’t care. Therefore we do not have to worry about what ends up on the register file’s Rb register specifier.
To keep things simple, we may just as well keep it the same as the R-type instruction and put the Rt field here.
So to summarize, this is how this datapath works. With Rs on Register File’s Ra input, bus A will get the value of Rs as the first ALU operand.
The second operand will come from the immediate field of the instruction.
Once the ALU complete the OR operation, the result will be written into the register specified by the instruction’s Rt field.
+3 = 50 min. (Y:30)

## Slide 13: 访存指令中的数据装入指令 (lw)
实现目标（7条指令）：
ADD and subtract
  add rd, rs, rt
  sub rd, rs, rt
OR Immediate:
  ori rt, rs, imm16
LOAD and STORE
  lw rt, rs, imm16
  sw rt, rs, imm16
BRANCH:
  beq rs, rt, imm16
JUMP:
  j target
3. 考虑lw 指令（访存指令的代表）
op
rs
rt
rd
shamt
func
0
6
11
16
21
26
31
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits
op
rs
rt
immediate
0
16
21
26
31
6 bits
16 bits
5 bits
5 bits
op
target address
0
26
31
6 bits
26 bits
Notes: In today’s lecture, I will show you how to implement the following subset of MIPS instructions: add, subtract, or immediate, load, store, branch, and the jump instruction.
The Add and Subtract instructions use the R format. The Op together with the Func fields together specified all the different kinds of add and subtract instructions.
Rs and Rt specifies the source registers. And the Rd field specifies the destination register.
The Or immediate instruction uses the I format. It only uses one source register, Rs. The other operand comes from the immediate field. The Rt field is used to specified the destination register.
Both the load and store instructions use the I format and both add the Rs and the immediate filed together to form the memory address.
The difference is that the load instruction will load the data from memory into Rt while the store instruction will store the data in Rt into the memory.
The branch on equal instruction also uses the I format. Here Rs and Rt are used to specify the registers we need to compare.
If these two registers are equal, we will branch to a location specified by the immediate field.
Finally, the jump instruction uses the J format and always causes the program to jump to a memory location specified in the address field.
I know I went over this rather quickly and you may have missed something. But don’t worry, this is just an overview. You will keep seeing these (point to the format) all day today.
+3 = 13 min. (X:53)

## Slide 14: RTL: The Load Instruction
lw rt, rs, imm16
  M[PC] 取指令（公共操作，取指部件完成）
  Addr ← R[rs] + SignExt(imm16) 计算存储单元地址 (符号扩展！)
  R[rt] ← M [Addr] 装入数据到寄存器rt中
  PC ← PC + 4 计算下地址（公共操作，取指部件完成）
immediate
0
16
15
31
16 bits
16 bits
0000 0000 00000 0000
0
0
16
15
31
immediate
16 bits
16 bits
1111 1111 1111 1111
1
符号扩展( 为什么不是零扩展? ) ：
思考：应在原数据通路上加哪些元件和连线？用何控制信号？
立即数用补码表示
op
rs
rt
immediate
0
16
21
26
31
6 bits
16 bits
5 bits
5 bits
Notes: Like the OR immediate instruction I just showed you, the load instruction also uses the I format (point to the format diagram).
But unlike the OR immediate instruction, the immediate field (Imm16 of the format diagram) is sign extended instead of zero extended.
That is we will duplicate the most significant bit of 16 times to the left to form a 32-bit value.
This sign extended value (SignExt) is then added to the register selected by the Rs field of the instruction to form the memory address.
The memory address is then used to load the value into the register specified by the Rt field of the instruction (Rt of the format diagram).
+2 = 57 min. (Y:37)

## Slide 15: 装入(lw)指令的数据通路
R[rt] ← M[ R[rs] + SignExt[imm16] ] lw rt, rs, imm16
32
ALUctr
Clk
busW
RegWr
32
32
busA
32
busB
5
5
5
Rw
Ra
Rb
32 32-bit
Registers
Rs
Rt
Don’t Care
(Rt)
Rd
RegDst
Mux
Mux
32
16
imm16
ALUSrc
ALU
加兰色部分。为什么？
控制信号RegDst, RegWr, ALUctr, ExtOp, ALUSrc, MemWr, MemtoReg 各取何值？
0
1
Ext
ExtOp
Mux
MemtoReg
Clk
Data In
WrEn
32
Adr
Data
Memory
32
MemWr
0
1
RegDst=1, RegWr=1, ALUctr=addu, ExtOp=1, ALUSrc=1, MemWr=0, MemtoReg=1
0:零扩展，1：符号扩展
0
1
op
rs
rt
imm16
0
16
21
26
31
6 bits
16 bits
5 bits
5 bits
Notes: Once again we cannot use the instruction’s Rd field for the Register File’s Rw input because load is a I-type instruction and there is no such thing as the Rd field in the I format.
So instead of Rd, the Rt field is used to specify the destination register through this two to one multiplexor.
The first operand of the ALU comes from busA of the register file which contains the value of Register Rs (points to the Ra input of the register file).
The second operand, on the other hand, comes from the immediate field of the instruction.
Instead of using the Zero Extender I used in datapath for the or immediate datapath, I have to use a more general purpose Extender that can do both Sign Extend and Zero Extend.
The ALU then adds these two operands together to form the memory address.
Consequently, the output of the ALU has to go to two places:
(a) First the address input of the data memory.
(b) And secondly, also to the input of this two-to-one multiplexer.
The other input of this multiplexer comes from the output of the data memory so we can place the output of the data memory onto the register file’s input bus for the load instruction.
For Add, Subtract, and the Or immediate instructions, the output of the ALU will be selected to be placed on the input bus of the register file.
In either case, the control signal RegWr should be asserted so the register file will be written at the end of the cycle.
+3 = 60 min. (Y:40)

## Slide 16: 访存指令中的存数指令 (sw)
实现目标（7条指令）：
ADD and subtract
  add rd, rs, rt
  sub rd, rs, rt
OR Immediate:
  ori rt, rs, imm16
LOAD and STORE
  lw rt, rs, imm16
  sw rt, rs, imm16
BRANCH:
  beq rs, rt, imm16
JUMP:
  j target
4. 考虑sw 指令（访存指令的代表）
op
rs
rt
immediate
0
16
21
26
31
6 bits
16 bits
5 bits
5 bits
op
rs
rt
rd
shamt
func
0
6
11
16
21
26
31
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits
op
target address
0
26
31
6 bits
26 bits
Notes: In today’s lecture, I will show you how to implement the following subset of MIPS instructions: add, subtract, or immediate, load, store, branch, and the jump instruction.
The Add and Subtract instructions use the R format. The Op together with the Func fields together specified all the different kinds of add and subtract instructions.
Rs and Rt specifies the source registers. And the Rd field specifies the destination register.
The Or immediate instruction uses the I format. It only uses one source register, Rs. The other operand comes from the immediate field. The Rt field is used to specified the destination register.
Both the load and store instructions use the I format and both add the Rs and the immediate filed together to form the memory address.
The difference is that the load instruction will load the data from memory into Rt while the store instruction will store the data in Rt into the memory.
The branch on equal instruction also uses the I format. Here Rs and Rt are used to specify the registers we need to compare.
If these two registers are equal, we will branch to a location specified by the immediate field.
Finally, the jump instruction uses the J format and always causes the program to jump to a memory location specified in the address field.
I know I went over this rather quickly and you may have missed something. But don’t worry, this is just an overview. You will keep seeing these (point to the format) all day today.
+3 = 13 min. (X:53)

## Slide 17: RTL: The Store Instruction
sw rt, rs, imm16
  M[PC] 取指令（公共操作，取指部件完成）
  Addr ← R[rs] + SignExt(imm16) 计算存储单元地址（符号扩展！）
  Mem[Addr] ← R[rt] 寄存器rt中的内容存到内存单元中
  PC ← PC + 4 计算下地址（公共操作，取指部件完成）
op
rs
rt
imm16
0
16
21
26
31
6 bits
16 bits
5 bits
5 bits
思考：应在原数据通路上加哪些元件和连线？用何控制信号？
Notes: Just like the load instruction:
(a) The store instruction also uses the I format.
(b) And the store instruction also forms the memory address by adding the contents
of the register selected by the Rs field to the sign extended immediate field.
However, unlike the load instruction, which gets data from memory and put the data into the the register file, the store instruction:
(a) Get the register selected by the Rt field of the instruction (R[rt]).
(b) And then write this register into the data memory.
+2 = 62 min. (Y:42)

## Slide 18: 存数(sw)指令的数据通路
M[ R[rs] + SignExt[imm16] ← R[rt] ] Example: sw rt, rs, imm16
32
ALUctr
Clk
busW
RegWr
32
32
busA
32
busB
5
5
5
Rw
Ra
Rb
32 32-bit
Registers
Rs
Rt
Rt
Rd
RegDst
Ext
Mux
Mux
32
16
imm16
ALUSrc
ExtOp
Mux
MemtoReg
Clk
Data In
WrEn
32
Adr
Data
Memory
32
MemWr
ALU
0
1
0
1
加兰色部分。为什么？
控制信号RegDst, RegWr, ALUctr, ExtOp, ALUSrc, MemWr, MemtoReg 各取何值？
RegDst=x, RegWr=0, ALUctr=addu, ExtOp=1, ALUSrc=1, MemWr=1, MemtoReg=x
0
1
op
rs
rt
imm16
0
16
21
26
31
6 bits
16 bits
5 bits
5 bits
Notes: And here is the datapath for the store instruction.
The Register File, the ALU, and the Extender are the same as the datapath for the load instruction because the memory address has to be calculated the exact same way:
(a) Put the register selected by Rs onto bus A and sign extend the 16 bit immediate field.
(b) Then make the ALU (ALUctr) adds these two (busA and output of Extender) together.
The new thing we added here is busB extension (DataIn).
More specifically, in order to send the register selected by the Rt field (Rb of the register file) to data memory, we need to connect bus B to the data memory’s Data In bus.
Finally, the store instruction is the first instruction we encountered that does not do any register write at the end.
Therefore the control unit must make sure RegWr is zero for this instruction.
+2 = 64 min. (Y:44)

## Slide 19: 分支（条件转移）指令（相等转移：beq）
实现目标（7条指令）：
ADD and subtract
  add rd, rs, rt
  sub rd, rs, rt
OR Immediate:
  ori rt, rs, imm16
LOAD and STORE
  lw rt, rs, imm16
  sw rt, rs, imm16
BRANCH:
  beq rs, rt, imm16
JUMP:
  j target
5. 考虑beq指令（条件转移指令的代表）
op
rs
rt
immediate
0
16
21
26
31
6 bits
16 bits
5 bits
5 bits
op
rs
rt
rd
shamt
func
0
6
11
16
21
26
31
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits
op
target address
0
26
31
6 bits
26 bits
Notes: In today’s lecture, I will show you how to implement the following subset of MIPS instructions: add, subtract, or immediate, load, store, branch, and the jump instruction.
The Add and Subtract instructions use the R format. The Op together with the Func fields together specified all the different kinds of add and subtract instructions.
Rs and Rt specifies the source registers. And the Rd field specifies the destination register.
The Or immediate instruction uses the I format. It only uses one source register, Rs. The other operand comes from the immediate field. The Rt field is used to specified the destination register.
Both the load and store instructions use the I format and both add the Rs and the immediate filed together to form the memory address.
The difference is that the load instruction will load the data from memory into Rt while the store instruction will store the data in Rt into the memory.
The branch on equal instruction also uses the I format. Here Rs and Rt are used to specify the registers we need to compare.
If these two registers are equal, we will branch to a location specified by the immediate field.
Finally, the jump instruction uses the J format and always causes the program to jump to a memory location specified in the address field.
I know I went over this rather quickly and you may have missed something. But don’t worry, this is just an overview. You will keep seeing these (point to the format) all day today.
+3 = 13 min. (X:53)

## Slide 20: RTL: The Branch Instruction
beq rs, rt, imm16
  M[PC] 取指令（公共操作，取指部件完成）
  Cond ← R[rs] - R[rt] 做减法比较rs和rt中的内容
  if (COND eq 0) 计算下地址（根据比较结果，修改PC）
    PC ← PC + 4 + ( SignExt(imm16) x 4 )
  else
    PC ← PC + 4
思考：立即数的含义是什么？是相对指令数还是相对单元数？
应在原数据通路上加哪些元件和连线？用什么控制信号来控制？
立即数用补码表示
op
rs
rt
imm16
0
16
21
26
31
6 bits
16 bits
5 bits
5 bits
Notes: How does the branch on equal instruction work?
Well it calculates the branch condition by subtracting the register selected by the Rt field from the register selected by the Rs field.
If the result of the subtraction is zero, then these two registers are equal and we take a branch. Otherwise, we keep going down the sequential path (PC <- PC +4).
+1 = 65 min. (Y:45)

## Slide 21: 条件转移指令的数据通路
beq rs, rt, imm16 We need to compare Rs and Rt !
ALUctr
Clk
busW
RegWr
32
32
busA
32
busB
5
5
5
Rw
Ra
Rb
32 32-bit
Registers
Rs
Rt
Rt
Rd
RegDst
Ext
Mux
Mux
32
16
imm16
ALUSrc
ExtOp
ALU
PC
Clk
Next Addr
Logic
16
imm16
Branch
To Instruction
Memory
Zero
思考：下址逻辑如何设计？
RegDst, RegWr, ALUctr, ExtOp, ALUSrc, MemWr, MemtoReg, Branch 各取何值？
RegDst=x, RegWr=0, ALUctr=subu, ExtOp=x, ALUSrc=0, MemWr=0, MemtoReg=x, Branch=1
0
1
0
1
op
rs
rt
imm16
0
16
21
26
31
6 bits
16 bits
5 bits
5 bits
Notes: The datapath for calculating the branch condition is rather simple.
All we have to do is feed the Rs and Rt fields of the instruction into the Ra and Rb inputs of the register file.
Bus A will then contain the value from the register selected by Rs.
And bus B will contain the value from the register selected by Rt.
The next thing to do is to ask the ALU to perform a subtract operation and feed the output Zero to the next address logic.
How does the next address logic block look like?
Well, before I show you that, let’s take a look at the binary arithmetics behind the program counter (PC).
+2 = 67 min. (Y:47)

## Slide 22: 下地址计算逻辑的设计
PC是一个32位地址:
  顺序执行时: PC<31:0> = PC<31:0> + 4
  转移执行时: PC<31:0> = PC<31:0> + 4 + SignExt[Imm16] X 4
MIPS按字节编址，每条指令为32位，占4个字节，故PC的值总是4的倍数，即后两位为00，因此，PC只需要30位即可。
下地址计算逻辑简化为：
顺序执行时: PC<31:2> = PC<31:2> + 1
  转移执行时: PC<31:2> = PC<31:2> + 1 + SignExt[Imm16]
  取指令时: 指令地址 = PC<31:2> 串接 “00”
PC采用30位后，其转移地址计算逻辑变得更加简单。
采用32位PC时，可用左移2位实现“X4”操作，计算转移地址用2个加法器！ 可以用更简便的方式实现如下：
Notes: In theory, the Program Counter (PC) is a 32-bit byte address into the Instruction memory.
The Program Counter is increment by four after each sequential instruction.
When a branch is taken, we need to sign extend the 16 bit immediate field, multiply this sign extended value by four, and add it to the sequential instruction address (PC + 4).
Why does this magic number “4” always come up? Well the reason is that the 32-bit PC is a byte address and all MIPS instructions are four bytes, or 32 bits, long.
In other words, if we keep a 32-bit Program Counter, then the two least significant bits of the Program Counter will always be zeros.
And if these two bits are always zeros, there is no reason to have hardware to keep them.
So in practice, we will simply the hardware by using a 30 bit program counter.
That is, we will build a Program Counter that only keep tracks of the upper 30 bits (<31:2>) of the instruction address because we know the 2 least significant bits will always be 0s.
Then instead of always increase the Program Counter by four for sequential operation, we only have to increase it by 1.
And for branch operation, we don’t need to multiply the sign extended immediate field by four before adding to the sequential PC (PC + 1).
And when we apply the program counter to the address of the instruction memory, we need to attach two zeros to its least significant bits.
+3 = 70 min. (Y:50)

## Slide 23: 下址逻辑设计
Using a 30-bit PC:
  顺序执行时: PC<31:2> = PC<31:2> + 1
  转移执行时: PC<31:2> = PC<31:2> + 1 + SignExt[Imm16]
  取指令时: 指令地址 = PC<31:2> concat “00”
30
30
SignExt
30
16
imm16
Mux
0
1
Adder
“1”
PC
Clk
Adder
30
30
Branch
Zero
Addr<31:2>
Instruction
Memory
Addr<1:0>
“00”
32
Instruction<31:0>
Instruction<15:0>
30
先根据当前PC取指令， 计算的下条指令地址在下一个时钟到来后才能写入PC！
标志位ZF，由ALU产生！
为什么这里没有用“ALU”而是用“Adder”? “ALU”和“Adder”有什么差别？
Notes: So let’s see how we can put all these theories (point to the equations) into practice.
The PC plus one is implemented by this first adder here.
For branch operation, we need to sign extend the immediate field of the instruction and then add it to the output of the first adder to implement this equation (PC + 1 + SignExt(imm16)).
For sequential operation, the output of the first adder is selected by the two-to-one mux so it will be saved into the PC register at the next clock tick.
For a taken branch, that is we have a branch_on_equal and the condition Zero is true, the output of the second adder is selected.
In all cases, the 30 bit Program Counter is used as instruction address bit 31 to bit 2.
The two least significant bits of the instruction address will always be zeroes.
One question you may want to ask is: Do we really need an adder just to add “1”?
Well may be not.
+2 = 72 min. (Y:52)

## Slide 24: 无条件转移指令
实现目标（7条指令）：
ADD and subtract
  add rd, rs, rt
  sub rd, rs, rt
OR Immediate:
  ori rt, rs, imm16
LOAD and STORE
  lw rt, rs, imm16
  sw rt, rs, imm16
BRANCH:
  beq rs, rt, imm16
JUMP:
  j target
6. 考虑Jump指令（无条件转移指令的代表）
op
rs
rt
immediate
0
16
21
26
31
6 bits
16 bits
5 bits
5 bits
op
rs
rt
rd
shamt
func
0
6
11
16
21
26
31
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits
op
target address
0
26
31
6 bits
26 bits
Notes: In today’s lecture, I will show you how to implement the following subset of MIPS instructions: add, subtract, or immediate, load, store, branch, and the jump instruction.
The Add and Subtract instructions use the R format. The Op together with the Func fields together specified all the different kinds of add and subtract instructions.
Rs and Rt specifies the source registers. And the Rd field specifies the destination register.
The Or immediate instruction uses the I format. It only uses one source register, Rs. The other operand comes from the immediate field. The Rt field is used to specified the destination register.
Both the load and store instructions use the I format and both add the Rs and the immediate filed together to form the memory address.
The difference is that the load instruction will load the data from memory into Rt while the store instruction will store the data in Rt into the memory.
The branch on equal instruction also uses the I format. Here Rs and Rt are used to specify the registers we need to compare.
If these two registers are equal, we will branch to a location specified by the immediate field.
Finally, the jump instruction uses the J format and always causes the program to jump to a memory location specified in the address field.
I know I went over this rather quickly and you may have missed something. But don’t worry, this is just an overview. You will keep seeing these (point to the format) all day today.
+3 = 13 min. (X:53)

## Slide 25: RTL: The Jump Instruction
j target
  M[PC] 取指令（公共操作，取指部件完成）
  PC<31:2> ← PC<31:28> 串接 target<25:0>
思考：应在原数据通路上加哪些元件和连线？
用什么控制信号来控制？
想一想：跳转指令的转移范围有多大？
是当前指令后面的0x000 0000~0xFFF FFFC 处？
不对！它不是相对寻址，而是绝对寻址
op
target address
0
26
31
6 bits
26 bits
Notes: Finally, let’s take a look at the jump instruction which uses the J format.
The effect of the jump instruction is to change the lower 26 bits of the Program Counter to the value specified in the address field of the instruction.
+1 = 76 min. (Y:46)

## Slide 26: Instruction Fetch Unit: 取指令部件
30
30
SignExt
30
16
imm16
Mux
0
1
Adder
“1”
PC
Clk
Adder
30
30
Branch
Zero
“00”
Addr<31:2>
Instruction
Memory
Addr<1:0>
32
j target
  PC<31:2> ← PC<31:28> concat target<25:0>
Instruction<15:0>
Instruction<31:0>
imm16、Target、…
30
26
4
Mux
1
0
Target
30
Jump
Instruc<25:0>
这是“取指部件”的完整设计
3 个输入: jump, Branch, Zero
1个输出: 指令字
PC的改变在下个Clk到达后发生！
RegDst, RegWr, ALUctr, ExtOp, ALUSrc, MemWr, MemtoReg, Branch, Jump 各取何值？
RegDst=ExtOp=ALUSrc=MemtoReg=ALUctr=x, RegWr=0, MemWr=0, Branch=0, Jump=1
Notes: Well this (points to the equation) is easy to implement.
All we have to do is grab the four most significant bits of the PC and put them right next to the 26 bits target, and we will have the next PC for the jump (point to the feedback path).
If we are running Powerview, what we will do now is to create a symbol called Instruction Fetch Unit.
The output of this symbol is the 32-bit instruction word.
The input to the Instruction Fetch Unit are two control signals, Branch and Jump, and one conditional input Zero from the datapath.
Using this new symbol, we can complete our single cycle datapath.
+2 = 78 min. (Y:58)

## Slide 27: The MIPS Subset(考察实现以下指令的数据通路)
ADD and subtract
  add rd, rs, rt
  sub rd, rs, rt
OR Immediate:
  ori rt, rs, imm16
LOAD and STORE
  lw rt, rs, imm16
  sw rt, rs, imm16
BRANCH:
  beq rs, rt, imm16
JUMP:
  j target
所有指令的数据通路都已设计好，合起来的数据通路是什么样的？
op
rs
rt
immediate
0
16
21
26
31
6 bits
16 bits
5 bits
5 bits
op
rs
rt
rd
shamt
func
0
6
11
16
21
26
31
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits
op
target address
0
26
31
6 bits
26 bits
Notes: In today’s lecture, I will show you how to implement the following subset of MIPS instructions: add, subtract, or immediate, load, store, branch, and the jump instruction.
The Add and Subtract instructions use the R format. The Op together with the Func fields together specified all the different kinds of add and subtract instructions.
Rs and Rt specifies the source registers. And the Rd field specifies the destination register.
The Or immediate instruction uses the I format. It only uses one source register, Rs. The other operand comes from the immediate field. The Rt field is used to specified the destination register.
Both the load and store instructions use the I format and both add the Rs and the immediate filed together to form the memory address.
The difference is that the load instruction will load the data from memory into Rt while the store instruction will store the data in Rt into the memory.
The branch on equal instruction also uses the I format. Here Rs and Rt are used to specify the registers we need to compare.
If these two registers are equal, we will branch to a location specified by the immediate field.
Finally, the jump instruction uses the J format and always causes the program to jump to a memory location specified in the address field.
I know I went over this rather quickly and you may have missed something. But don’t worry, this is just an overview. You will keep seeing these (point to the format) all day today.
+3 = 13 min. (X:53)

## Slide 28: 综合所有指令的数据通路（此处为单周期的数据通路）
32
ALUctr
Clk
busW
RegWr
32
32
busA
32
busB
5
5
5
Rw
Ra
Rb
32 32 bit
Registers
Rs
Rt
Rt
Rd
RegDst
Ext
Mux
Mux
32
16
imm16
ALUSrc
ExtOp
Mux
MemtoReg
Clk
Data In
WrEn
32
Adr
Data
Memory
32
MemWr
ALU
Instruction
Fetch Unit
Clk
Zero
Instruction<31:0>
Jump
Branch
0
1
0
1
0
1
<21:25>
<16:20>
<11:15>
<0:15>
Imm16
Rd
Rt
Rs
指令执行结果总是在下个时钟到来时开始保存在 寄存器 或 存储器 或 PC 中！
下一讲考虑：如何产生控制信号！（控制器的设计内容）
Notes: So here is the single cycle datapath we just built.
If you push into the Instruction Fetch Unit, you will see the last slide showing the PC, the next address logic, and the Instruction Memory.
Here I have shown how we can get the Rt, Rs, Rd, and Imm16 fields out of the 32-bit instruction word.
The Rt, Rs, and Rd fields will go to the register file as register specifiers while the Imm16 field will go to the Extender where it is either Zero and Sign extended to 32 bits.
The signals ExtOp, ALUSrc, ALUctr, MemWr, MemtoReg, RegDst, RegWr, Branch, and Jump are control signals.
And I will show you how to generate them in the next class..
+2 = 80 min. (Z:00)