## Slide 1: 第 15 讲
单周期处理设计-控制逻辑单元

## Slide 2: 学习内容
考察每条指令在数据通路中的执行过程和涉及到的控制信号的取值
  公共操作：取指令和计算下址PC
  R-Type指令（add / sub）
  立即数指令 （ori）
  访存指令（lw / sw）
  分支指令 （beq）
  跳转指令 （j）
汇总各指令的控制信号取值
  分两类控制信号：直接送往数据通路 / 送往局部控制单元
分析ALU操作对应的控制信号与func字段之间的关系
设计ALU局部控制单元
设计主控制单元

## Slide 3: Add / Sub操作开始时取指部件中的动作
30
30
SignExt
30
16
imm16
Mux
0
1
Adder
“1”
PC
Adder
30
30
Branch = previous
Zero = previous
“00”
Addr<31:2>
Instruction
Memory
Addr<1:0>
32
Mux
1
0
26
4
PC<31:28>
Target
30
取指令: Instruction ← M[PC]
  所有指令都相同
Jump = previous
Instruction<15:0>
Instruction<31:0>
30
Instr<25:0>
Clk
新指令还没有取出译码，所以控制信号的值还是原来指令的旧值。
新指令还没有执行，所以标志也为旧值。
取出指令的第31-26位作为操作码首先被译码。op=000000, 则为R-type指令
取指部件由旧控制信号控制，会不会有问题？
没有问题！Why?
因为在下个Clk到来之前PC输入端的值不会写入，只要保证下个Clk来之前能产生正确的PC即可！
Notes: First let’s look at the Instruction Fetch Unit where everything begins.
Every instruction begins at the clock tick. The clock tick in this case is the high to low transition of the Clk (points to the “bubble” of PC).
What happens right after the clock tick?
After Clk-to-Q delay, the PC gets the value that points to the Add instruction and fetch the add instruction from the memory but sending the address to the Ideal Instruction memory.
Notice that since this is the beginning of the instruction, Control signals Branch and Jump will still have the old values from the previous instruction.
At the beginning of ALL instructions execution, the instruction unit behaves the same way as shown here and we won’t repeat this picture for every instruction.
+2 = 12 min. (X:52)

## Slide 4: 指令译码后R型指令（Add / Sub）操作过程
32
ALUctr = Add or Sub
Clk
busW
RegWr = 1
32
32
busA
32
busB
5
5
5
Rw
Ra
Rb
32 32-bit
Registers
Rs
Rt
Rt
Rd
RegDst = 1
Ext
Mux
Mux
32
16
imm16
ALUSrc = 0
ExtOp = x
Mux
MemtoReg = 0
Clk
Data In
WrEn
32
Adr
Data
Memory
32
MemWr = 0
ALU
Instruction
Fetch Unit
Clk
Zero
Instruction<31:0>
Jump = 0
Branch = 0
R[rd] ← R[rs] + / - R[rt]
0
1
0
1
0
1
<21:25>
<16:20>
<11:15>
<0:15>
Imm16
Rd
Rt
Rs
op
rs
rt
rd
shamt
func
0
6
11
16
21
26
31
Notes: This picture shows the activities at the main datapath during the execution of the Add or Subtract instructions.
The active parts of the datapath are shown in different color as well as thicker lines.
First of all, the Rs and Rt of the instructions are fed to the Ra and Rb address ports of the register file and cause the contents of registers specified by the Rs and Rt fields to be placed on busA and busB, respectively.
With the ALUctr signals set to either Add or Subtract, the ALU will perform the proper operation and with MemtoReg set to 0, the ALU output will be placed onto busW.
The control we are going to design will also set RegWr to 1 so that the result will be written to the register file at the end of the cycle.
Notice that ExtOp is don’t care because the Extender in this case can either do a SignExt or ZeroExt. We DON’T care because ALUSrc will be equal to 0--we are using busB.
The other control signals we need to worry about are:
(a) MemWr has to be set to zero because we do not want to write the memory.
(b) And Branch and Jump, we have to set to zero. Let me show you why.
+3 = 15 min. (X:55)

## Slide 5: R型指令（Add /Sub）最后阶段取指部件中的动作
30
30
SignExt
30
16
imm16
Mux
0
1
Adder
“1”
PC
Clk
Adder
30
30
Branch = 0
Zero = x
“00”
Addr<31:2>
Instruction
Memory
Addr<1:0>
32
Mux
1
0
26
4
PC<31:28>
Target
30
PC ← PC + 4
  除 Branch and Jump以外的指令都相同
Jump = 0
Instruction<15:0>
Instruction<31:0>
30
Instruction<25:0>
因为新的控制信号保证了正确的PC值的产生，在足够长的时间后，下个时钟Clk到来！
Notes: This picture shows the control signals setting for the Instruction Fetch Unit at the end of the Add or Subtract instruction.
Both the Branch and Jump signals are set to 0.
Consequently, the output of the first adder, which implements PC plus 1, is selected through the two 2-to-1 mux and got placed into the input of the Program Counter register.
The Program Counter is updated to this new value at the next clock tick.
Notice that the Program Counter is updated at every cycle. Therefore it does not have a Write Enable signal to control the write.
Also, this picture is the same for or all instructions other than Branch and Jump.
Therefore I will only show this picture again for the Branch and Jump instructions and will not repeat this for all other instructions.
+2 = 17 min. (X:57)

## Slide 6: Register-Register（R型指令） Timing
32
Result
ALUctr
Clk
busW
RegWr
32
32
busA
32
busB
5
5
5
Rw
Ra
Rb
32 32-bit
Registers
Rs
Rt
Rd
ALU
Clk
PC
Rs, Rt, Rd,
Op, Func
Clk-to-Q
ALUctr
Instruction Memory Access Time
Old Value
New Value
RegWr
Old Value
New Value
Delay through Control Logic
busA, B
Register File Access Time
Old Value
New Value
busW
ALU Delay
Old Value
New Value
Old Value
New Value
New Value
Old Value
Register Write
Occurs Here
PC+4
PC+4 PC
Notes: Let’s take a more quantitative picture of what is happening.
At each clock tick, the Program Counter will present its latest value to the Instruction memory after Clk-to-Q time(虽然早就产生，但PC值的改变一定在时钟边沿的控制下进行的).
After a delay of the Instruction Memory Access time, the Opcode, Rd, Rs, Rt, and Function fields will become valid on the instruction bus.
Once we have the new instruction, that is the Add or Subtract instruction, on the instruction bus, two things happen in parallel.
First of all, the control unit will decode the Opcode and Func field and set the control signals ALUctr and RegWr accordingly. We will cover this in the next lecture.
While this is happening (points to Control Delay), we will also be reading the register file (Register File Access Time).
Once the data is valid on busA and busB, the ALU will perform the Add or Subtract operation based on the ALUctr signal.
Hopefully, the ALU is fast enough that it will finish the operation (ALU Delay) before the next clock tick.
At the next clock tick, the output of the ALU will be written into the register file because the RegWr signal will be equal to 1.
+3 = 45 min. (Y:25)
Complement:
Instruction bus: see slide 12 on An Abstract View of the Critical Path

## Slide 7: ori 指令译码后的执行过程
32
ALUctr = or
Clk
busW
RegWr = 1
32
32
busA
32
busB
5
5
5
Rw
Ra
Rb
32 32-bit
Registers
Rs
Rt
Rt
Rd
RegDst = 0
Ext
Mux
Mux
32
16
imm16
ALUSrc = 1
ExtOp = 0
Mux
MemtoReg = 0
Clk
Data In
WrEn
32
Adr
Data
Memory
32
MemWr = 0
ALU
Instruction
Fetch Unit
Clk
Zero
Instruction<31:0>
Jump = 0
Branch = 0
R[rt] ← R[rs] or ZeroExt[Imm16]
0
1
0
1
0
1
<21:25>
<16:20>
<11:15>
<0:15>
Imm16
Rd
Rt
Rs
op
rs
rt
immediate
0
16
21
26
31
Notes: Now let’s look at the control signals setting for the Or immediate instruction.
The OR immediate instruction OR the content of the register specified by the Rs field to the Zero Extended Immediate field and write the result to the register specified in Rt.
This is how it works in the datapath. The Rs field is fed to the Ra address port to cause the contents of register Rs to be placed on busA.
The other operand for the ALU will come from the immediate field. In order to do this, the controller need to set ExtOp to 0 to instruct the extender to perform a Zero Extend operation.
Furthermore, ALUSrc must set to 1 such that the MUX will block off bus B from the register file and send the zero extended version of the immediate field to the ALU.
Of course, the ALUctr has to be set to OR so the ALU can perform an OR operation.
The rest of the control signals (MemWr, MemtoReg, Branch, and Jump) are the same as theAdd and Subtract instructions.
One big difference is the RegDst signal. In this case, the destination register is specified by the instruction’s Rt field, NOT the Rd field because we do not have a Rd field here.
Consequently, RegDst must be set to 0 to place Rt onto the Register File’s Rw address port.
Finally, in order to accomplish the register write, RegWr must be set to 1.
+3 = 20 min. (X:60)

## Slide 8: Load指令译码后的执行过程
32
ALUctr = addu
Clk
busW
RegWr = 1
32
32
busA
32
busB
5
5
5
Rw
Ra
Rb
32 32-bit
Registers
Rs
Rt
Rt
Rd
RegDst = 0
Ext
Mux
Mux
32
16
imm16
ALUSrc = 1
ExtOp = 1
Mux
MemtoReg = 1
Clk
Data In
WrEn
32
Adr
Data
Memory
32
MemWr = 0
ALU
Instruction
Fetch Unit
Clk
Zero
Instruction<31:0>
Jump = 0
Branch = 0
0
1
0
1
0
1
<21:25>
<16:20>
<11:15>
<0:15>
Imm16
Rd
Rt
Rs
R[rt] ← Data Memory {R[rs] + SignExt[imm16]}
op
rs
rt
immediate
0
16
21
26
31
ALUtcr应为add还是addu？差别在于溢出标志！
Notes: Let’s continue our lecture with the load instruction. What does the load instruction do?
It first adds the contents of the register specified by the Rs field to the Sign Extended version of the Immediate field to form the memory address.
Then it uses this memory address to access the memory and write the data back to the register specified by the Rt field of the instruction.
Here is how the datapath works: first the Rs field is fed to the Register File’s Ra address port to place the register onto bus A.
Then the ExtOp signal is set to 1 so that the immediate field is Sign Extended and we place this value (output of Extender) onto the ALU input by setting ALUsrc to 1.
The ALU then add (ALUctr = add) the two together to form the memory address which is then placed onto the Data Memory’s address port.
In order to place the Data Memory’s output bus onto the Register File’s input bus (busW), the control needs to set MemtoReg to 1.
Similar to the OR immediate instruction I showed you earlier, the destination register here is specified by the Rt field. Therefore RegDst must be set to 0.
Finally, RegWr must be set to 1 to complete the register write operation.
Well, it should be obvious to you guys by now that we need to set Branch and Jump to 0 to make sure the Instruction Fetch Unit update the Program Counter correctly.
+3 = 28 min. (Y:08)

## Slide 9: Store指令译码后的执行过程
32
ALUctr = addu
Clk
busW
RegWr = 0
32
32
busA
32
busB
5
5
5
Rw
Ra
Rb
32 32-bit
Registers
Rs
Rt
Rt
Rd
RegDst = x
Ext
Mux
Mux
32
16
imm16
ALUSrc = 1
ExtOp = 1
Mux
MemtoReg = x
Clk
Data In
WrEn
32
Adr
Data
Memory
32
MemWr = 1
ALU
Instruction
Fetch Unit
Clk
Zero
Instruction<31:0>
Jump = 0
Branch = 0
0
1
0
1
0
1
<21:25>
<16:20>
<11:15>
<0:15>
Imm16
Rd
Rt
Rs
M{R[rs] + SignExt[imm16]} ← R[rt]
op
rs
rt
immediate
0
16
21
26
31
Notes: The store instruction performs the inverse function of the load. Instead of loading data from memory, the store instruction sends the contents of register specified by Rt to data memory.
Similar to the load instruction, the store instruction needs to read the contents of register Rs (points to Ra port) and add it to the sign extended verion of the immediate filed (Imm16, ExtOp = 1, ALUSrc = 1) to form the data memory address (ALUctr = add).
However unlike the Load instructoion where busB is not used, the store instruction will use busB to send the data to the Data memory.
Consequently, the Rt field of the instruction has to be fed to the Rb port of the register file.
In order to write the Data Memory properly, the MemWr signal has to be set to 1.
Notice that the store instruction does not update the register file. Therefore, RegWr must be set to zero and consequently control signals RegDst and MemtoReg are don’t cares.
And once again we need to set the control signals Branch and Jump to zero to ensure proper Program Counter updataing.
Well, by now, you are probably tied of these boring stuff where Branch and Jump are zero so let’s look at something different--the bracnh instruction.
+3 = 31 min. (Y:11)

## Slide 10: Branch指令译码后的执行过程
32
ALUctr = subu
Clk
busW
RegWr = 0
32
32
busA
32
busB
5
5
5
Rw
Ra
Rb
32 32-bit
Registers
Rs
Rt
Rt
Rd
RegDst = x
Ext
Mux
Mux
32
16
imm16
ALUSrc = 0
ExtOp = x
Mux
MemtoReg = x
Clk
Data In
WrEn
32
Adr
Data
Memory
32
MemWr = 0
ALU
Instruction
Fetch Unit
Clk
Zero
Instruction<31:0>
Jump = 0
Branch = 1
0
1
0
1
0
1
<21:25>
<16:20>
<11:15>
<0:15>
Imm16
Rd
Rt
Rs
if (R[rs] - R[rt] == 0) then Zero ← 1 ; else Zero ← 0
op
rs
rt
immediate
0
16
21
26
31
Notes: So how does the branch instruction work?
As far as the main datapath is concerned, it needs to calculate the branch condition. That is, it subtracts the register specified in the Rt field from the register specified in the Rs field and set the condition Zero accordingly.
In order to place the register values on busA and busB, we need to feed the Rs and Rt fields of the instruction to the Ra and Rb ports of the register file and set ALUSrc to 0.
Then we have to instruction the ALU to perform the subtract (ALUctr = sub) operation and set the Zero bit accordingly.
The Zero bit is sent to the Instruction Fetch Unit. I will show you the internal of the Instruction Fetch Unit in a second.
But before we leave this slide, I want you to notice that ExtOp, MemtoReg, and RegDst are don’t cares but RegWr and MemWr have to be ZERO to prevent any write to occur.
And finally, the controller needs to set the Branch signal to 1 so the Instruction Fetch Unit knows what to do. So now let’s take a look at the Instruction Fetch Unit.
+2 = 33 min. (Y:13)

## Slide 11: Branch指令最后阶段取指部件中的动作
30
30
SignExt
30
16
imm16
Mux
0
1
Adder
“1”
PC
Clk
Adder
30
30
Branch = 1
Zero = 1
“00”
Addr<31:2>
Instruction
Memory
Addr<1:0>
32
Mux
1
0
26
4
PC<31:28>
Target
30
Jump = 0
Instruction<15:0>
Instruction<31:0>
30
Instruction<25:0>
if (Zero == 1) then PC = PC + 4 + SignExt[imm16]*4 ; else PC = PC + 4
op
rs
rt
immediate
0
16
21
26
31
Notes: Let’s look at the interesting case where the branch condition Zero is true (Zero = 1).
Well, if Zero is not asserted, we will have our boring case where PC + 1 is selected.
Anyway, with Branch = 1 and Zero = 1, the output of the second adder will be selected.
That is, we will add the sequential address, that is output of the first adder, to the sign extended version of the immediate field, to form the branch target address (output of 2nd adder).
With the control signal Jump set to zero, this branch target address will be written into the Program Counter register (PC) at the end of the clock cycle.
+2 = 35 min. (Y:15)

## Slide 12: Jump指令译码后的执行过程
32
ALUctr = x
Clk
busW
RegWr = 0
32
32
busA
32
busB
5
5
5
Rw
Ra
Rb
32 32-bit
Registers
Rs
Rt
Rt
Rd
RegDst = x
Ext
Mux
Mux
32
16
imm16
ALUSrc = x
ExtOp = x
Mux
MemtoReg = x
Clk
Data In
WrEn
32
Adr
Data
Memory
32
MemWr = 0
ALU
Instruction
Fetch Unit
Clk
Zero
Instruction<31:0>
Jump = 1
Branch = 0
0
1
0
1
0
1
<21:25>
<16:20>
<11:15>
<0:15>
Imm16
Rd
Rt
Rs
IFU中目标地址送PC，其他什么都不做（只要保证存储部件不发生写的动作）
op
target address
0
26
31
如何保证存储部件不发生写？
使相应的写使能信号为0！
Notes: The control signals setting in the main datapath for the Jump instruction is pretty boring because in most cases, we DON’T CARE.
More specifically, control signals ExtOp, ALUSrc, ALUctr are all don’t cares because the ALU is not used at all for the Jump instruction.
Control signals MemtoReg and RegDst are don’t are because Jump does not write the register file. That is the reason why we still need to set RegWr to zero.
Furthermore, we also need to set MemWr to zero to avoid Data Memroy write.
Finally, the control signal Branch is set to zero but Jump is set to 1.
+2 = 37 min. (X:17)
Complement: So far as we have already seen, almost all instructions use ALU. But this jump instruction is exceptional.
which instruction doesn't use ALU?

## Slide 13: Jump指令结束前IFU中的动作
30
30
SignExt
30
16
imm16
Mux
0
1
Adder
“1”
PC
Clk
Adder
30
30
Branch = 0
Zero = x
“00”
Addr<31:2>
Instruction
Memory
Addr<1:0>
32
Mux
1
0
26
4
PC<31:28>
Target
30
PC ← PC<31:29> concat target<25:0> concat “00”
Jump = 1
Instruction<15:0>
Instruction<31:0>
30
Instruction<25:0>
op
target address
0
26
31
Notes: Inside the Instruction Fetch Unit, with Branch set to zero and Jump set to 1, we will not use the output of neither Adder.
What we will use is the concatenation of the four most significant bits of the current program counter and the twenty six bits of the target address.
With the control signal Jump set to 1, this value will be send to the Program Counter and get written into PC at the next clock tick (points to the Clk bubble).
+2 = 39 min. (Y:19)
There should be an improvement: When Jump=1, we don’t have to set Branch=0. We can set Branch=x to simply logical design of the control part. But we have to set Jump=0 when Branch=1.

## Slide 14: 综合分析结果，得到如下指令与控制信号的关系表
add
sub
ori
lw
sw
beq
jump
RegDst
ALUSrc
MemtoReg
RegWrite
MemWrite
Branch
Jump
ExtOp
ALUctr<2:0>
1
0
0
1
0
0
0
x
add
1
0
0
1
0
0
0
x
sub
0
1
0
1
0
0
0
0
or
0
1
1
1
0
0
0
1
addu
x
1
x
0
1
0
0
1
addu
x
0
x
0
0
1
0
x
subu
x
x
x
0
0
0
1
x
xxx
op
target address
op
rs
rt
rd
shamt
func
0
6
11
16
21
26
31
op
rs
rt
immediate
R-type
I-type
J-type
add, sub
ori, lw, sw, beq
jump
func
op
00 0000
00 0000
00 1101
10 0011
10 1011
00 0100
00 0010
10 0000
10 0010
与func字段无关！
Notes: Here is a table summarizing the control signals setting for the seven (add, sub, ...) instructions we have looked at.
Instead of showing you the exact bit values for the ALU control (ALUctr), I have used the symbolic values here.
The first two columns are unique in the sense that they are R-type instrucions and in order to uniquely identify them, we need to look at BOTH the op field as well as the func fiels.
Ori, lw, sw, and branch on equal are I-type instructions and Jump is J-type. They all can be uniquely idetified by looking at the opcode field alone.
Now let’s take a more careful look at the first two columns. Notice that they are identical except the last row.
So we can combine these two rows here if we can “delay” the generation of ALUctr signals.
This lead us to something called “local decoding.”
+3 = 42 min. (Y:22)

## Slide 15: 主控制单元和ALU局部控制单元
R-type
ori
lw
sw
beq
jump
RegDst
ALUSrc
MemtoReg
RegWrite
MemWrite
Branch
Jump
ExtOp
ALUctr
1
0
0
1
0
0
0
x
Add/Sub
0
1
0
1
0
0
0
0
Or
0
1
1
1
0
0
0
1
Addu
x
1
x
0
1
0
0
1
Addu
x
0
x
0
0
1
0
x
Subu
x
x
x
0
0
0
1
x
xxx
op
00 0000
00 1101
10 0011
10 1011
00 0100
00 0010
MIPS指令格式中指示操作性质的字段有两个：op(主控) 和 func（ALU局控）。
ALUctr的值：
非R型指令时，取决于ALUop;
R型指令时，
取决于func。
3
ALU
func
Main
Control
op
6
ALU
Control
(Local)
6
ALUop
ALUctr
R-Type
0
1
Notes: That is, instead of asking the Main Control to generates the ALUctr signals directly (see the diagram with the ALU), the main control will generate a set of signals called ALUop.
For all I and J type instructions, ALUop will tell the ALU Control exactly what the ALU needs to do (Add, Subtract, ...) .
But whenever the Main Control sees a R-type instructions, it simply throws its hands up and say: “Wow, I don’t know what the ALU has to do but I know it is a R-type instruction” and let the Local Control Block, ALU Control to take care of the rest.
Notice that this save us one column from the table we had on the last slide. But let’s be honest, if one column is the ONLY thing we save, we probably will not do it.
But when you have to design for the entire MIPS instruction set, this column will used for ALL R-type instructions, which is more than just Add and Subtract I showed you here.
Another advantage of this table over the last one, besides being smaller, is that we can uniquely identify each column by looking at the Op field only.
Therefore, as I will show you later, the Main Control ONLY needs to look at the Opcode field.
How many bits do we need for ALUop?
+3 = 45 min. (Y:25)

## Slide 16: ALUop的逻辑表达式
ALUop的编码定义如下：
R型指令时，ALUctr与func有关，需建立ALUctr 与func之间对应关系
func
Main
Control
op
6
ALU
Control
(Local)
N=?
6
ALUop
ALUctr
R-Type
0
1
ALUop<2>=beq=!op<5>&!op<4>&!op<3>&op<2>&!op<1>&!op<0> (op=000100)
ALUop<1>=ori=!op<5>&!op<4>&op<3>&op<2>&!op<1>&op<0> (op=001101)
ALUop<0>= R-type=!op<5>&!op<4>&!op<3>&!op<2>&!op<1>&!op<0> (op=000000)
R-type
ori
lw
sw
beq
jump
运算
由func指定
or
addu
addu
subu
xxx
ALUop<2:0>
xx1
010
000
000
100
xxx
指令
Notes: What this table and diagram implies is that if the ALU Control receives ALUop = 100, it has to decode the instruction’s “func” field to figure out what the ALU needs to do.
Based on the MIPS encoding in Appendix A of your text book, we know we have a Add instruction if the func field is 10 000.
If the func field is 10 0010, we know we have a subtract operation and so on.
Notice that the bit 5 and bit 4 of this field is the same for all these operations so as far as the ALU control is concerned, these bits are don’t care.
Now recall from your ALU homework, the ALUctr signals has the following meaning (point to the table): 000 means Add, 001 means subtract, ... etc.
Based on these three tables (point to the last row of the top table and then the two other tables) and the fact that bit 5 and bit 4 of the “func” field are don’t care, we can derive the following truth table for ALUctr.
+2 = 48 min. (Y:28)

## Slide 17: ALU局部控制器逻辑表达式
ALUctr<0> =!func<2> & !func<0>
func<5:0>
Instruction Operation
10 0000
10 0010
10 0011
10 1010
10 1011
add
sub
subu
slt
sltu
ALUctr<2:0>
ALU Operation
001
101
100
111
110
add
sub
subu
slt
sltu
ALU
ALUctr<1> = func<3> & !func<2> & func<1>
ALUctr<2> = !func<2> & func<1>
func
Main
Control
op
6
ALU
Control
(Local)
N=?
6
ALUop
ALUctr
R-Type
0
1
000000
rs
rt
rd
shamt
func
0
6
11
16
21
26
31
R-type
Notes: From the truth table we had before the break, we can derive the logic equation for ALUctr bit 2 by collecting all the rows that has ALUCtr bit 2 equals to 1 and this table is the result.
Each row becomes a product term and we need to OR the product terms together.
Notice that the last row are identical except the bit<3> of the func fields. One is zero and the other is one. Together, they make bit<3> a don’t care term.
With all these don’t care terms, the logic equation is rather simple.
The first product term is: not ALUOp<2> and ALUOp<0>.
The second product term, after we making Func<3> a don’t care becomes ...
+2 = 57 min. (Y:37)

## Slide 18: 主控制单元的真值表
R-type
ori
lw
sw
beq
jump
RegDst
ALUSrc
MemtoReg
RegWrite
MemWrite
Branch
Jump
ExtOp
ALU运算
1
0
0
1
0
0
0
x
“R-type”
0
1
0
1
0
0
0
0
Or
0
1
1
1
0
0
0
1
Addu
x
1
x
0
1
0
0
1
Addu
x
0
x
0
0
1
0
x
Subu
x
x
x
0
0
0
1
x
xxx
op
00 0000
00 1101
10 0011
10 1011
00 0100
00 0010
ALUop <2>
x
0
0
0
1
x
ALUop <1>
x
1
0
0
0
x
ALUop <0>
1
0
0
0
0
x
Main
Control
op
6
ALU
Control
(Local)
func
3
6
ALUop
ALUctr
3
RegDst
ALUSrc
:
主控单元的输入
主控单元的输出
R-type
1
0
0
0
0
0
R-Type
1
0
Notes: Now that we have taken care of the Local Control (ALU Control), let’s refocus our attention to the Mian Controller.
The job of the Main Control is to look at the Opcode field of the instruction and generate these control signals for the datapath (RegDst, ... ExtOp) as well as the 3-bit ALUop field for the ALU Control.
Here, I have shown you the symbolic value of the ALUop field as well as the actual bit assignment.
For example here (2nd column), the R-type ALUop is encode as 100 and the Add operation (3rd column) is encoded as 000..
This is call a quote “Truth Table” unquote because if you think about it, this is like having the truth table rotates 90 degrees.
Let me show you what I mean by that.
+3 = 65 min. (Y:45)

## Slide 19: 考察每个控制信号的逻辑方程（如：RegWrite）
R-type
ori
lw
sw
beq
jump
RegWrite
1
1
1
0
0
0
op
00 0000
00 1101
10 0011
10 1011
00 0100
00 0010
RegWrite = R-type + ori + lw
  = !op<5> & !op<4> & !op<3> & !op<2> & !op<1> & !op<0> (R-type)
  + !op<5> & !op<4> & op<3> & op<2> & !op<1> & op<0> (ori)
  + op<5> & !op<4> & !op<3> & !op<2> & op<1> & op<0> (lw)
op<0>
op<5>
.
.
op<5>
.
.
<0>
op<5>
.
.
<0>
op<5>
.
.
<0>
op<5>
.
.
<0>
op<5>
.
.
<0>
R-type
ori
lw
sw
beq
jump
RegWrite
指令译码器
Notes: For example, consider the control signal RegWrite.
If we treat all the don’t cares as zeros, this row here means RegDest has to be equal to one whenever we have a R-type, or an OR immediate, or a load instruction.
Since we can determine whether we have any of these instructions (point to the column headers) by looking at the bits in the “OP” field, we can transform this symbolic equation to this binary logic equation.
For example, the first product term here say we have a R-type instruction whenever all the bits in the “OP” field are zeros.
So each of these big AND gates implements one of the columns (R-type, ori, ...) in our table. Or in more technical terms, each AND gate implements a product term.
In order to finish implementing this logic equation, we have to OR the proper terms together.
In the case of the RegWrite signal, we need to OR the R-type, ORi, and load terms together.
+2 = 67 min. (Y:47)

## Slide 20: Main Control的PLA实现
op<0>
op<5>
.
.
op<5>
.
.
<0>
op<5>
.
.
<0>
op<5>
.
.
<0>
op<5>
.
.
<0>
op<5>
.
.
<0>
R-type
ori
lw
sw
beq
jump
RegWrite
ALUSrc
MemtoReg
MemWrite
Branch
Jump
RegDst
ExtOp
ALUop<0>
ALUop<1>
ALUop<2>
指令译码器
Notes: Similarly, for ALUSrc, we need to OR the ori, load, and store terms together because we need to assert the ALUSrc signals whenever we have the Ori, load, or store instructions.
The RegDst, MemtoReg, MemWrite, Branch, and Jump signals are very simple. They don’t need to OR any product terms together because each is asserted for only one instruction.
For example, RegDst is asserted ONLY for R-type instruction and MemtoReg is asserted ONLY for load instruction.
ExtOp, on the other hand, needs to be set to 1 for both the load and store instructions so the immediate field is sign extended properly.
Therefore, we need to OR the load and store terms together to form the signal ExtOp.
Finally, we have the ALUop signals.
But clever encoding of the ALUop field, we are able to keep them simple so that no OR gates is needed.
If you don’t already know, this regular structure with an array of AND gates followed by another array of OR gates is called a Programmable Logic Array, or PLA for short.
It is one of the most common ways to implement logic function and there are a lot of CAD tools available to simplify them.
+3 = 70 min. (Y:50)